Coverstar Automatic Pool Cover Switch Wiring

Direct Electric Drive

# Text boxes

SWITCH

Standard

2 ¾”x 4 ½” x

2 ⅜ ” deep

weatherproof  Corlon single gang box for switch

(4 screw holes – 1 in each corner – to mount switch)

Locking switch lid will not fit if switch is mounted in a double gang box.

Switch should be mounted 5 feet above floor and where operator will have a full view of the pool.

3 Wires in from panel

110 v., 9 amp, GFI protected circuit.

Black (hot)

White (neutral)

Green (ground)

4 wires out to cover motor

Red & Blue (directionals)

White (neutral)

Green (ground)

Wire Terminal Locations on Back of Switch

Black (hot)

Red (directonal)

Blue (directonal)

Green (ground)

Note: There are two thin black wires coming from the green pilot light on the switch faceplate. The wire with the forked end terminal is attached to the switch at the red (directional) screw. The other wire is to be joined with the white (neutral) wires.

After final wiring, if the cover movement doesn’t agree with the “Cover” – “Uncover” labels on the front of the switch, just reverse the positions of the red and blue wires on the switch.

The white (neutral) wires are not attached to the switch. They are just joined to each other with a wire nut.

Questions?

Call Superior Pool Covers

1-800-636-3137

MOTOR IN COVER PIT

110 Volt, 9 Amp, ¾ hp.

Motor has 2’ of flexible conduit ending in ½” male threaded connector to attach to junction box in pit.